Analysis of Multiwavelength Data

1. Import
-Import data as normal
-look at each wavelength, under multi-wavelength lambda controls to ensure that the OD is within readable range for all <1.2OD

2. Edit Data
- You only need to edit one triple per channel
-Edit as normal, ensure “Save too all Wavelengths” is checked

3. Time Derivative
-You can use this program to see what s-value fitting range you should use. You want to delete the scans that have minimal diffuse at the start of the run, and at the end of the data you want to delete all scans that no longer have a plateau

4. Performing 2DSA
-Send all of the triples for a 2DSA
-Check to ensure that they all fit well, you can use the program called Query Model RMSDs to ensure that all RMSDs are in a reasonable range

5. Fit meniscus
-This is only done on one wavelength, usually one that is the middle of the ranges measured.
-When selecting the meniscus in the “Fit Meniscus” program, ensure that “apply to all wavelengths” is checked. This will change the menisci for for all triples of that channel

6. Preform 2DSA-IT
-Send all of the triples for a 2DSA
-Check to ensure that they all fit well, you can use the program called Query Model RMSDs to ensure that all RMSDs are in a reasonable range

7. Simulating the experiment so that all wavelengths have the sample time states
-Open Multiwavelength --> Optima MWL fit simulation
-Prefilter models – select the run
- Select models – select all models from 1 channel
- Select buffer – water (density=0.99239, viscosity=1.00199)
- Simulation Parameters: Set the run time and speed
-If your run was done at 20°C you can use the exact same parameters as in the original run
-If your run was done at any other temperature, your simulation will be performed at 20°C because you are using the modeled data which is correct the water at 20°C. Therefore the run speed and time may need to changed as temperature affects the buffers density and viscosity. Apply parameters that result in similar experimental boundaries to the original run.
- Select a rotor – simulation rotor
- Start simulation
- Save: It will save into your imports file with the letters “ISSF” before the run name

8. Import and edit the ISSF file
-When importing the data tell it that it was measured in the simulation rotor, and with a simulation centerpiece
-The solution needs to be remade with water as the buffer

9. Edit Data
- You only need to edit one triple; it will apply it to all triples if “save too all Wavelengths”

10. Optical deconvolution
- Open Multiwavelength --> Mwl species fit
- Load experiment – load the ISSF file
- Load species fits – load the extinction profiles of the species present in the sample
-These files are made by collecting a dilution series of the pure spectral contributors individually and then the spectra from the different concentrations are globally fit together using the “Spectrum fitter”, and produces and .extinction file when saved
- Species Fit data → Okay
- Save Data: It will save into your imports file with the letters “SSF-ISSF” before the run name

11. Import the SSF-ISSF files
-When importing the data tell it that it was measured in the simulation rotor, and with a simulation centerpiece
-The solution needs to be remade with water as the buffer

12. Edit Data
- If you deconvoluted in molar concentrations the y-axis value will be very small so you will need to zoom into the data to see it.
-You only need to edit one of the triples; it will apply if to both
-Edit as normal, ensure “save too all Wavelengths” is checked

13. Analysis – 2DSA-IT (do not need a 2DSA or FM)
-The SSF-ISSF data can directly be put into the van Holde-Weischet program
-You can also perform a 2DSA-IT fit directly on this data, without time or radially invariant noise selected.
-No need to do a 2DSA or FM fit first